## Slide 1
BRAIN WAVES × ARTIFICIAL INTELLIGENCE · TUTORIAL #2
The Shape of
Brain Data
Where does a number like 576 × 22 × 1125 come from? Let's build it up, one piece at a time.
A lesson built from braindecode · the BCI Competition IV 2a dataset
Notes: Tutorial #2. Last time we trained a tiny AI on brain signals. Today we zoom in on ONE thing: the shape of the data — 576 clips x 22 channels x 1125 samples, at 250 Hz, 4.5 seconds per clip. It looks scary; it's really just multiplication. We'll build every number.

## Slide 2
THE NUMBER WE'RE DECODING
This one line describes the whole dataset
576 clips × 22 channels × 1125 samples
250 Hz · 4.50 seconds per clip
Four questions unlock it:
How FAST?
250 snapshots every second (250 Hz).
How LONG?
4.5 s per clip → 1125 samples.
How MANY sensors?
22 electrodes = 22 channels.
How MANY clips?
576 labeled trials in total.
Notes: Roadmap for the deck. The whole dataset is one line of numbers. To understand it, answer four questions: how fast we sample, how long each clip is, how many sensors, and how many clips. Each is one slide, each is simple multiplication.

## Slide 3
PIECE 1 · HOW FAST
250 Hz = 250 snapshots
every second
The EEG doesn't record a smooth line — it takes super-fast snapshots of the voltage, over and over.
'Hz' (hertz) means 'times per second'. 250 Hz = 250 snapshots each second.
Think of a movie camera: enough snapshots per second and it looks like smooth motion.
1 second
÷ 250 snapshots
= one snapshot every
4 milliseconds
1000 ms ÷ 250 = 4 ms between snapshots
Notes: Piece 1: sampling rate. 250 Hz means 250 measurements per second. 1000 milliseconds divided by 250 = 4 ms between snapshots — that's the '4 ms per sample' you see in the app. Camera analogy: fast enough snapshots look like smooth motion.

## Slide 4
PIECE 2 · HOW LONG
One clip is 4.5 seconds long
We don't feed the AI the whole recording — we cut it into short clips, one per 'imagine a movement' moment.
Each clip starts 0.5 s before the go-cue and lasts to 4.0 s after it: that's 4.5 seconds.
How many snapshots is that? Multiply the length by the speed.
one clip
= 4.50 seconds
4.5 s × 250 samples/s = 1125 samples
That's why every clip is 1125 samples 'tall' in time.
Notes: Piece 2: clip length. A clip runs from 0.5 s before the cue to 4.0 s after = 4.5 seconds. Length times speed: 4.5 s x 250 samples/s = 1125 samples. That is the 1125 in the shape — the number of time-steps in one clip.

## Slide 5
PIECE 3 · HOW MANY SENSORS
22 channels = 22 sensors
listening at once
The EEG cap in this dataset has 22 electrodes over the parts of the brain that plan movement.
Each electrode is one 'channel' — its own stream of snapshots.
So at every moment in time, we don't get one number — we get 22, one per sensor.
22 sensors
= 22 rows of numbers, all recorded at the same time.
Notes: Piece 3: channels. 22 electrodes on the scalp = 22 channels. At each time-step you don't get one voltage, you get 22 — one per sensor. That is the 22 in the shape.

## Slide 6
PUT PIECES 1–3 TOGETHER
One clip is a grid of numbers
22 channels going down × 1125 time-snapshots going across
22 channels →
1125 samples (time) →
numbers in ONE clip
22 × 1125
= 24,750
numbers, for a single 4.5-second clip.
(The app shows a slice of this exact grid when you click 'View the windows'.)
Notes: Combine pieces 1-3: one clip is a grid, 22 channels tall by 1125 samples wide. 22 x 1125 = 24,750 numbers in a single clip. This is exactly the table the web app shows in 'View the windows'.

## Slide 7
PIECE 4 · HOW MANY CLIPS
Where does 576 come from?
4 movements
Left hand · Right hand · Feet · Tongue — the 4 labels.
72 tries each
The person repeats each movement 72 times.
2 days
Recorded in 2 sessions on different days.
4 movements × 72 tries = 288 per day
288 × 2 days = 576 clips
Notes: Piece 4: how many clips. 4 movements, each imagined 72 times = 288 clips in one session. Recorded across 2 days = 288 x 2 = 576 clips total for one person. That's the 576.

## Slide 8
THE WHOLE STACK
Stack every clip into one big box
Stack all 576 clips and you get a 3-D box of numbers — scientists call it a tensor.
Its shape is exactly: 576 clips × 22 channels × 1125 samples.
Multiply them out to see how much data that really is.
576 × 22 × 1125
= 14,256,000
numbers — over 14 million!
X = the box of clips (576, 22, 1125) y = 576 labels, one movement per clip
Notes: Stack all 576 clips: a 3-D box (a tensor) shaped 576 x 22 x 1125. Multiply: that's 14,256,000 numbers — over 14 million — for one subject. The box is X; the 576 labels are y. Same X/y idea as Tutorial #1, just much bigger.

## Slide 9
YOU DID THE MATH
Now the shape makes sense
250 Hz → a snapshot every 4 ms. 4.5 s × 250 = 1125 samples per clip.
22 sensors → 22 channels. One clip = 22 × 1125 = 24,750 numbers.
4 movements × 72 tries × 2 days = 576 clips. Whole box = 576 × 22 × 1125 = 14,256,000.
▶ Try it: open Tutorial #2 in the BrainWerks app and click 'View the windows' — you'll see these exact numbers.
Notes: Recap: every number in 576 x 22 x 1125 came from simple counting and multiplication — speed, length, sensors, and how many clips. Then send them to the app's Tutorial #2 and click 'View the windows' to see the real thing.